## Slide 1: ELEC 3050 Lab Project
Ethan Cook

## Slide 2: Overview
Micro-
controller
Motor drive
Motor
Tachometer
Signal Conditioning
Keypad
AND Gates

## Slide 3: Keypad (Requirement A)
AND the row signals to generate a keypad interrupt signal
Reads rows then columns
Inputs are configured with pull-up resistors

## Slide 4: Motor Drive (Requirement C)
Motor can receive 15V
GPIO PA0 outputs PWM signal
Flyback diode needed to protect circuit
MOSFET transistor is used

## Slide 5: Signal Conditioning
Need to convert max 20V AC signal to max 3.3V DC signal
Uses a bridge rectifier, attenuator, and lowpass filter

## Slide 6: Counter (Requirement D)
Counter period is in the range of 792 ms to 808 ms
Counter starts/stops (*) and counts up/down (#)
Counter value rolls over

## Slide 8: PWM Signal (Requirement B)
Produces 4 kHz PWM signal
10 different duty cycles to choose from
Duty cycles selected by keypad (0-A)

## Slide 10: Feedback Control (Requirement E)
ADC read values range between 0x000 and 0xE00
Desired speeds set at 0x300, 0x600, 0x900, and 0xC00
Keypad “D” used to cycle between desired speeds
Sampling every 12.5 ms
Speed 1
Speed 2
Speed 3
Speed 4
Off

## Slide 11: PID Controller
Proportional
Control output is proportional to the current error
Proportional term alone results in a residual error
Integral
Control output is a function of current error and past error
Integral term eliminates residual error
Derivative
Control output is a prediction of future error
Derivative term estimates future trends of error
P
I
D
∑
∑
Process
Desired
Actual
+
+
+
+
-

## Slide 12
Feedback Control: Off to Speed 1
Feedback Control: Finger pressure

## Slide 13: Issues During the Project
ADC input errors
Inputs would jump around 0x400
Feedback control wouldn’t work
Troubleshot
Fixed configuration
Keypad Debounce
Buttons are double pressed with an interval of around 60 ms
Swapped keypads
Added delay in code

## Slide 14: Thank you
Ethan Cook
efc0009@auburn.edu